## Slide 1: CAMERAS
Slides are from Svetlana Lazebnik

## Slide 2: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 3: Understanding Real Cameras

## Slide 4: Home-Made Pinhole Camera
http://www.debevec.org/Pinhole/
Slide by A. Efros

## Slide 5: Shrinking the Aperture
Why not make the aperture as small as possible?
  Less light gets through
  Diffraction effects…
Slide by Steve Seitz

## Slide 6: Shrinking the Aperture

## Slide 7: Adding a lens

## Slide 8: Adding a Lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
Slide by Steve Seitz

## Slide 9: Adding a Lens
A lens focuses light onto the film
  Thin lens model:
    Rays passing through the center are not deviated (pinhole projection model still holds)
    All parallel rays converge to one point on a plane located at the focal length f
Slide by Steve Seitz
focal point
f

## Slide 10: Adding a Lens
A lens focuses light onto the film
  There is a specific distance at which objects are “in focus”
    other points project to a “circle of confusion” in the image
“circle of
confusion”
Slide by Steve Seitz

## Slide 11: Thin Lens Formula
What is the relation between the focal length ( f ), the distance of the object from the optical center (D), and the distance at which the object will be in focus (D′)?
f
D
D′
Slide by Frédo Durand
object
image plane
lens
Notes: This is the relation between the focal length (f), the distance of the object from the camera (D), and the distance at which the object will be in focus (D’)

## Slide 12: Thin Lens Formula
f
D
D′
Similar triangles everywhere!
Slide by Frédo Durand
object
image plane
lens

## Slide 13: Thin Lens Formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = D′/D
Slide by Frédo Durand
object
image plane
lens

## Slide 14: Thin Lens Formula
f
D
D′
Similar triangles everywhere!
y′
y
y′/y = (D′−f )/f
Slide by Frédo Durand
object
image plane
lens
y′/y = D′/D

## Slide 15: Thin Lens Formula
f
D
D′
1
D′
D
1
1
f
+
=
Any point satisfying the thin lens equation is in focus.
Slide by Frédo Durand
object
image plane
lens
Notes: And the set of all such points forms a plane parallel to the image (plane of focus).
Uses of the formula: given focal length and depth in scene that you want to be in focus, it tells you where to put the image plane. Given f and distance of image plane from camera center, it tells you which depth in the scene will be in focus.

## Slide 16: Depth of Field
http://www.cambridgeincolour.com/tutorials/depth-of-field.htm
Slide by A. Efros
Notes: Depth of field is the distance between the nearest and farthest objects in a scene that appear acceptably sharp in an image (Wikipedia)

## Slide 17: Controlling Depth of Field
http://en.wikipedia.org/wiki/File:Depth_of_field_illustration.svg
Changing the aperture size affects depth of field
  A smaller aperture increases the range in which the object is approximately in focus
  But small aperture reduces amount of light – need to increase exposure

## Slide 18: Varying the Aperture
Large aperture = small DOF
Small aperture = large DOF
Slide by A. Efros

## Slide 19: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?
Source: Lazebnik.

## Slide 20: Field of view
The field of view is the angular extent of the world observed by the camera (Wikipedia)
What determines the FOV?
  Focal length (), length of the sensor ():
  Larger focal length = smaller FOV
f
Source: Lazebnik.

## Slide 21: Field of View
Slide by A. Efros
Notes: The field of view is the angular extent of the world that is observed by the camera.

## Slide 22: Field of View
Slide by A. Efros

## Slide 23: Field of View / Focal Length
Large FOV, small f
Camera close to car
Small FOV, large f
Camera far from the car
Sources: A. Efros, F. Durand

## Slide 24: Same Effect for Faces
standard
wide-angle
telephoto
Source: F. Durand

## Slide 25: Approximating an Orthographic Camera
Source: Hartley & Zisserman

## Slide 26: The Dolly Zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
http://en.wikipedia.org/wiki/Dolly_zoom

## Slide 27: The Dolly Zoom
Continuously adjusting the focal length while the camera moves away from (or towards) the subject
“The Vertigo shot”
Example of dolly zoom from Goodfellas (YouTube)
Example of dolly zoom from La Haine (YouTube)

## Slide 28: Choice of Lens and Viewpoint: A COVID-Era Illustration
Source

## Slide 29: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations

## Slide 30: Real Lenses

## Slide 31: Lens Flaws: Vignetting

## Slide 32: Lens Flaws: Radial Distortion
No distortion
Pin cushion
Barrel
  Caused by imperfect lenses
  Deviations are most noticeable near the edge of the lens

## Slide 33: Lens flaws: Spherical Aberration
Spherical lenses don’t focus light perfectly
Rays farther from the optical axis focus closer

## Slide 34: Lens Flaws: Chromatic Aberration
Lens has different refractive indices for different wavelengths: causes color fringing
Near Lens Center
Near Lens Outer Edge

## Slide 35: Overview
Cameras with lenses
  Depth of field
  Field of view
  Lens aberrations
Digital sensors

## Slide 36: Digital Camera
A digital camera replaces film with a sensor array
  Each cell in the array is light-sensitive diode that converts photons to electrons
  Two common types
    Charge Coupled Device (CCD)
    Complementary metal oxide semiconductor (CMOS)
  http://electronics.howstuffworks.com/digital-camera.htm
Slide by Steve Seitz

## Slide 37: Color filter arrays
Source: Steve Seitz
Demosaicing:
Estimation of missing components from neighboring values
Why more green?
Bayer grid (1976)
Human Luminance Sensitivity Function

## Slide 38: Color filter arrays
Demosaicing:
Estimation of missing components from neighboring values
Recent cameraphone technology: pixel binning
Bayer grid (1976)

## Slide 39: Problem with Demosaicing: Color Moire
Slide by F. Durand

## Slide 40: The Cause of Color Moire
detector
Fine black and white detail in image
misinterpreted as color information
Slide by F. Durand

## Slide 41: Misc. digital camera artifacts
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
In-camera processing
    oversharpening can produce halos
Compression
    JPEG artifacts, blocking
Blooming
    CCD charge overflowing into neighboring pixels
Color artifacts
    Color moire
    Purple fringing from microlenses

## Slide 42: Digital Camera Artifacts
Noise
    low light is where you most notice noise
    light sensitivity (ISO) / noise tradeoff
    stuck pixels
In-camera processing
    oversharpening can produce halos
Compression
    JPEG artifacts, blocking
Blooming
    charge overflowing into neighboring pixels
Color artifacts
    purple fringing from microlenses,
    white balance
Slide by Steve Seitz

## Slide 43: Historic Milestones
Pinhole model: Mozi (470-390 BCE), Aristotle (384-322 BCE)
Principles of optics (including lenses): Alhacen (965-1039 CE)
Camera obscura: Leonardo da Vinci (1452-1519), Johann Zahn (1631-1707)
First photo: Joseph Nicephore Niepce (1822)
Daguerréotypes (1839)
Photographic film (Eastman, 1889)
Cinema (Lumière Brothers, 1895)
Color Photography (Lumière Brothers, 1908)
Television (Baird, Farnsworth, Zworykin, 1920s)
First consumer camera with CCD Sony Mavica (1981)
First fully digital camera: Kodak DCS100 (1990)
Niepce, “La Table Servie,” 1822
Alhacen’s notes
Old television camera

## Slide 44: First Digitally Scanned Photograph
1957, 176x176 pixels
http://listverse.com/history/top-10-incredible-early-firsts-in-photography/
Notes: From the website: “Russell Kirsch was a computer pioneer at the National Institute of Standards and Technology in the USA when he developed the system by which a camera could be fed into a computer. The photo is of Kirsch’s three month old son Walden and it measured a mere 176×176 pixels. Baby Walden now works in communications for Intel.”

## Slide 45: Camera Sales Over Time
Source
Notes: CIPA: Camera & Imaging Products Association

## Slide 46: Camera Sales Over Time
The full chart…
Source
More information on color and cameras:
https://www.eecs.yorku.ca/~mbrown/ICCV19_Tutorial_MSBrown.pdf
Notes: CIPA: Camera & Imaging Products Association