## Slide 1: Epipolar Geometry
Slides are from Svetlana Lazebnik
Note in Prof. Lazenik’s slides: Many slides adapted from J. Johnson and D. Fouhey

## Slide 2
Epipolar plane
Baseline
Epipoles
Epipolar lines
Left view
Right view

## Slide 3: Outline
Epipolar geometry setup
Epipolar constraint
Essential matrix
Fundamental matrix
Estimating the fundamental matrix

## Slide 4: Epipolar Geometry Setup
Suppose we have two cameras with centers ,
The baseline is the line connecting the origins

## Slide 5: Epipolar Geometry Setup
Epipoles , are where the baseline intersects the image planes, or projections of the other camera in each view

## Slide 6: Epipolar Geometry Setup
Consider a point , which projects to and

## Slide 7: Epipolar Geometry Setup
The plane formed by , , and is called an epipolar plane
There is a family of planes passing through and

## Slide 8: Epipolar Geometry Setup
Epipolar lines connect the epipoles to the projections of
Equivalently, they are intersections of the epipolar plane with the image planes – thus, they come in matching pairs

## Slide 9: Epipolar Geometry Setup: Summary
Epipolar plane
Baseline
Epipoles
Epipolar lines

## Slide 10: Example Configuration: Converging cameras

## Slide 11: Example Configuration: Converging Cameras
Epipoles are finite, may be visible in the image

## Slide 12: Example Configuration: Motion Parallel to Image Plane
Where are the epipoles and what do the epipolar lines look like?

## Slide 13: Example configuration: Motion Parallel to Image Plane
Epipoles infinitely far away, epipolar lines parallel

## Slide 14: Example Configuration: Motion Parallel to Image Plane

## Slide 15: Example configuration: Motion Perpendicular to Image Plane

## Slide 16: Example configuration: Motion Perpendicular to Image Plane

## Slide 17: Example Configuration: Motion Perpendicular to Image Plane
Epipole is “focus of expansion” and coincides with the principal point of the camera
Epipolar lines go out from principal point

## Slide 18: Outline
Epipolar geometry setup
Epipolar constraint

## Slide 19: Epipolar Constraint
Suppose we observe a single point in one image

## Slide 20: Epipolar constraint
Where can we find the corresponding to in the other image?

## Slide 21: Epipolar Constraint
Where can we find the corresponding to in the other image?
Along the epipolar line corresponding to (projection of visual ray connecting with into the second image plane)

## Slide 22: Epipolar Constraint
Similarly, all points in the left image corresponding to have to lie along the epipolar line corresponding to

## Slide 23: Epipolar constraint
Potential matches for have to lie on the matching epipolar line
Potential matches for have to lie on the matching epipolar line

## Slide 24: Epipolar Constraint: Example

## Slide 25: Epipolar constraint
Whenever two points and lie on matching epipolar lines and , the visual rays corresponding to them meet in space, i.e., and could be projections of the same 3D point

## Slide 26: Epipolar Constraint
Remember: in general, two rays do not meet in space!

## Slide 27: Epipolar Constraint
Caveat: if and satisfy the epipolar constraint, this doesn’t mean they have to be projections of the same 3D point

## Slide 28: Outline
Epipolar geometry setup
Epipolar constraint
Essential matrix

## Slide 29: Math of the Epipolar Constraint: Calibrated Case
Assume the intrinsic and extrinsic parameters of the cameras are known, world coordinate system is set to that of the first camera
Then the projection matrices are given by and
We can pre-multiply the projection matrices (and the image points) by the inverse calibration matrices to get normalized image coordinates:

## Slide 30: Math of the epipolar constraint: Calibrated case
We have
This means the three vectors , , and are linearly dependent
This constraint can be written using the triple product

## Slide 31: Math of the epipolar constraint: Calibrated case
Recall:

## Slide 32: Math of the epipolar constraint: Calibrated case
Essential Matrix
H. C. Longuet-Higgins. A computer algorithm for reconstructing a scene from two projections. Nature 293 (5828): 133–135, September 1981

## Slide 33: The Essential Matrix

## Slide 34: The Essential Matrix: Properties
is the epipolar line associated with ()
  Recall: a line is given by or where and

## Slide 35: The Essential Matrix: Properties
is the epipolar line associated with ()
is the epipolar line associated with ()
and
is singular (rank two) and has five degrees of freedom

## Slide 36: Outline
Epipolar geometry setup
Epipolar constraint
Essential matrix
Fundamental matrix

## Slide 37: Epipolar Constraint: Uncalibrated Case
The calibration matrices and of the two cameras are unknown
We can write the epipolar constraint in terms of unknown normalized coordinates:
,
where ,

## Slide 38: Epipolar Constraint: Uncalibrated Case
, where
Fundamental Matrix
Faugeras et al., (1992), Hartley (1992)

## Slide 39: The Fundamental Matrix

## Slide 40: The Fundamental Matrix: Properties
is the epipolar line associated with ()
is the epipolar line associated with ()
and
is singular (rank two) and has seven degrees of freedom

## Slide 41: Outline
Epipolar geometry setup
Epipolar constraint
Essential matrix
Fundamental matrix
Estimating the fundamental matrix

## Slide 42: Estimating the Fundamental Matrix
Given: correspondences and

## Slide 43: Estimating the Fundamental Matrix
Given: correspondences and
Constraint:

## Slide 44: The Eight Point Algorithm
Homogeneous least squares to find :
Eigenvector of with smallest eigenvalue

## Slide 45: Enforcing Rank-2 Constraint
We know needs to be singular/rank 2. How do we force it to be singular?
Solution: take SVD of the initial estimate and throw out the smallest singular value

## Slide 46: Enforcing Rank-2 Constraint
Initial estimate
Rank-2 estimate

## Slide 47: Normalized Eight Point Algorithm
Recall that are pixel coordinates. What might be the order of magnitude of each column of ?
This causes numerical instability!

## Slide 48: The Normalized Eight-Point Algorithm
In each image, center the set of points at the origin, and scale it so the mean squared distance between the origin and the points is 2 pixels
Use the eight-point algorithm to compute from the normalized points
Enforce the rank-2 constraint
Transform fundamental matrix back to original units: if and are the normalizing transformations in the two images, then the fundamental matrix in original coordinates is
R. Hartley. In defense of the eight-point algorithm. TPAMI 1997

## Slide 49: Nonlinear Estimation
Linear estimation minimizes the sum of squared algebraic distances between points and epipolar lines (or points and epipolar lines ):
Nonlinear approach: minimize sum of squared geometric distances
xi

## Slide 50: Comparison of Estimation Algorithms
 | 8-point | Normalized 8-point | Nonlinear least squares
Av. Dist. 1 | 2.33 pixels | 0.92 pixel | 0.86 pixel
Av. Dist. 2 | 2.18 pixels | 0.85 pixel | 0.80 pixel

## Slide 51: Seven-Point Algorithm
Set up least squares system with seven pairs of matches and solve for null space (two vectors) using SVD
Solve for polynomial equation to get coefficients of linear combination of null space vectors that satisfies
Source: e.g., M. Pollefeys tutorial (2000)

## Slide 52: From Epipolar Geometry to Camera Calibration
Estimating the fundamental matrix is known as “weak calibration”
If we know the calibration matrices of the two cameras, we can estimate the essential matrix:
The essential matrix gives us the relative rotation and translation between the cameras, or their extrinsic parameters
Alternatively, if the calibration matrices are known (or in practice, if good initial guesses of the intrinsics are available), the five-point algorithm can be used to estimate relative camera pose
D. Nister. An efficient solution to the five-point relative pose problem. IEEE Trans. PAMI, 2004

## Slide 53: The Fundamental Matrix Song
http://danielwedge.com/fmatrix/